## Slide 1: Swapping Cutters

## Slide 2: Swapping Cutters in Creo
Select cutter to be swapped
Select parent in cutter group in Model Tree
Right click > Edit Actions > Replace selected component or UDF
Be sure to separate pads if grouped to ensure pads are assigned unique names
  Open gauge pad surface group
  Copy-paste (ctrl+c, ctrl+v) surface group
  Options > "Exclude surfaces and Fill holes"
  Using Ctrl+left click select surfaces elements to be deleted
  Repeat until each pad is its own unique surface group

## Slide 3: Swapping Cutters in Creo
Check Unrelated Component
Under Select New Component, open the explorer and navigate to replacement cutter
Click Ok
Click Yes on pop-up

## Slide 4: Swapping Cutters in Creo
Expand part section at bottom
Click on ORIG to align new part with old part (new part with turn orange)
Click OK at top ribbon
1
2
3

## Slide 5: Last Slide