## Slide 1: Assembly Coordinate System

## Slide 2: Editing Coordinate System
Select Coordinate System in "Model Tree" Dialog Box (Boxed in red)
Model Tab > Datum Ribbon > Coordinate System
Name > DYNAMIC_CSYS

## Slide 3: Orienting Coordinate System
Set Orientation Objects
Match Axis Orientation as shown (Use Flip)
  X axis oriented parallel to blade 1 face
  Y axis oriented down when X axis due right
  Z axis oriented to drillstring

## Slide 4: Part Coordinate System

## Slide 5: Creating Coordinate System / Setting Origin
Select Parts (Boxed in red depending on "Body 1" elements)
Model Tab > Datum Ribbon > Coordinate System
Name > DYNAMIC_CSYS

## Slide 6: Orienting Coordinate System
Set Orientation Objects
Match Axis Orientation as shown on next slides (Use Flip)
  X axis set normal to cutter face
  Y axis pointing to right when looking into X axis with Z axis pointing up
  Z axis set normal to cutting contact point

## Slide 9: Tagging

## Slide 10: Bit Tagging
Tag gauge pad surface only (highlighted green in image)
Be sure to separate pads if grouped to ensure pads are assigned unique names
  Open gauge pad surface group
  Copy-paste (ctrl+c, ctrl+v) surface group
  Options > "Exclude surfaces and Fill holes"
  Using Ctrl+left click select surfaces elements to be deleted
  Repeat until each pad is its own unique surface group

## Slide 11: Cutter Tagging
Tag cutter elements as shown in image
Cutter chamfer (edge surface)
Cutter face
Cutter body
(all remaining pieces not chamfer or face)
Cutter face
Cutter body
(all remaining pieces not chamfer or face)

## Slide 12: Last Slide